## Slide 1
LAYERED SCENARIO MODEL
How the AV scenario
simulator works
And what the delivered 2-million-mile run actually tells us
6
independent scenario layers
→
1
joint scenario tuple at any instant
Delivered configuration: 2,000,000 miles at 50 mph
Results and mechanism walkthrough

## Slide 2
LAYERED SCENARIO MODEL
It estimates unknown-scenario exposure—not vehicle safety risk
02
The simulator answers a coverage question:
“How often, and for how long, does a modeled scenario enter an unknown state?”
What it does
• samples categorical scenario elements
• evolves each layer over time
• tracks contiguous unknown episodes
• reports exposure, duration, and rate
What it does not do
No physical dynamics, perception errors, collision model, or calibrated real-world risk estimate.
DRIVE
2M mi
40,000 simulated hours
SPEED
50 mph
constant conversion from time to miles
OUTPUT
Episodes
starts, durations, overlaps and rates
Sources: README.md; DOCUMENTATION.md; config.yaml

## Slide 3
LAYERED SCENARIO MODEL
Six independent layers form every scenario tuple
03
Each layer has its own dwell-time distribution and transition probabilities. The joint scenario changes whenever any layer changes.
Layer
Examples of what it represents
Mean dwell
Element unknowns?
street
route composition
300 s
No
temporal modifications
work zones / traffic management
600 s
Yes
ego maneuver
AV maneuver class
30 s
Yes
road-user maneuver
other road-user maneuver
45 s
Yes
environment
weather / lighting
1,800 s
No
triggering conditions
unexpected AV context
120 s
Yes
Independence is an intentional simplifying assumption: there are no conditional links between layers.
Source: config.yaml; simulator.py (LAYER_DEFINITIONS)

## Slide 4
LAYERED SCENARIO MODEL
Each sampled layer gets a fixed probability model
04
The street layer is special: its 12 configured route-composition probabilities are used exactly, without a Dirichlet draw.
1
Choose count
Sample an element count from the layer’s configured range.
↓
2
Assign rarity
Use largest-remainder category counts, then shuffle labels across elements.
↓
3
Set weights
Common → very rare weights; solve the unknown weight for a 0.4% designed mass.
↓
4
Draw probabilities
One Dirichlet draw at concentration 20,000 creates the transition vector.
↓
5
Draw dwell times
Gamma(shape = μ²/var, scale = var/μ), clamped to ≥1 second.
Target unknown-element mass: 0.4%
Sources: config.yaml; simulator.py (build_layer, compute_unknown_weight)

## Slide 5
LAYERED SCENARIO MODEL
The engine jumps directly to the next layer expiry
05
At any instant, every layer has a remaining dwell time. The loop advances by the minimum of those times, then updates only expired layers.
01
Current state
six current elements
+six remaining times
→
02
Find next event
dt = min(remaining)
→
03
Advance
time += dt
miles += 50·dt / 3600
→
04
Transition
sample next element
and new Gamma duration
→
05
Track
update episodes and
combination matches
Why it matters
The delivered 2M-mile run advances through 9,998,505 event steps in about 46 seconds—not 144 million one-second iterations.
Sources: simulator.py (ScenarioSimulator.run_resumable); results/summary.md

## Slide 6
LAYERED SCENARIO MODEL
Episodes measure continuous unknown occupancy
06
This avoids inflating counts when a slow unknown condition persists while unrelated fast layers change around it.
Layer transition
Action
Meaning
known → unknown
open
A new element episode starts.
unknown → known
close
The current element episode ends.
unknown A → unknown B
close + open
A different unknown gets its own episode.
unknown A → unknown A
continue
A self-transition does not split the episode.
known → known
nothing
No element episode is active.
Key consequence: element episodes are per layer and may overlap; changes in other layers do not start or end them.
Source: simulator.py (episode_transition_action and event loop); README.md

## Slide 7
LAYERED SCENARIO MODEL
Three distinct mechanisms are tracked at the same time
07
All episode types contribute to the “unknown time” union, but they answer different questions.
ELEMENT
Unknown element
A single layer occupies an element labelled “unknown.” Starts and ends follow the occupancy rules.
PATTERN
Known interaction
A configured conjunction across ≥2 layers, e.g. a particular street state + weather state. Survives unrelated changes.
HASH
Unknown tuple
A deterministic SHA-256 classifier flags ~0.5% of all-known six-layer tuples. Ends on any tuple change.
Element episode
+
Pattern episode
+
Hash episode
= union time in “an unknown scenario” (overlaps counted once)
Sources: README.md; simulator.py (CombinationRule and UnknownCombinationClassifier)

## Slide 8
DELIVERED 2M-MILE RUN
84,296 unknown episodes came from three different mechanisms
08
The headline total blends element-level novelty with two synthetic combination mechanisms.
Chart: 
| Element | Pattern | Hash combination
Episodes | 39227 | 3476 | 41593
RATE
42,148 / 1M mi
Episode starts per million miles
UNION TIME
2.7408%
3,946,822 seconds of simulated time
COMPLETION
0 truncated
No episodes remained open at run end
Source: results/summary.md; results/stats.json

## Slide 9
DELIVERED 2M-MILE RUN
Short dwell times drive more episode starts
09
All four unknown-capable layers target 0.4% unknown selection. Episode counts still differ sharply because their dwell times differ.
Chart: 
| Temporal | Ego | Road-user | Triggering
Element episodes | 977 | 21018 | 12217 | 5015
Element episodes by layer
EGO MANEUVER
21,018
Mean dwell: 30 s → most frequent opportunities to start an episode.
ROAD-USER MANEUVER
12,217
Mean dwell: 45 s → second highest turnover rate.
TEMPORAL MODIFICATIONS
977
Mean dwell: 600 s → far fewer transition opportunities.
Source: results/summary.md; results/stats.json

## Slide 10
DELIVERED 2M-MILE RUN
Duration reveals what ends each kind of episode
10
Mean duration
ELEMENT
60.5 s
Ends when that layer leaves its unknown element.
PATTERN
261.0 s
Ends only when a referenced layer breaks the rule.
HASH COMBINATION
16.7 s
Ends on any genuine tuple change.
Sources: results/summary.md; results/plots/episode_durations.png

## Slide 11
DELIVERED 2M-MILE RUN
Episode starts are steady at scale, but modestly more variable than Poisson
11
WINDOW MEAN
421.5
episode starts per 10,000 miles
(200 complete windows)
DISPERSION INDEX
1.261
variance / mean
1.0 would be ideal Poisson
Interpretation
Near-Poisson starts are consistent with independent rare transitions, but the process is not exactly Poisson.
Sources: results/summary.md; results/plots/window_counts.png; analytical_model.md

## Slide 12
LAYERED SCENARIO MODEL
Use the simulator for coverage and sensitivity—not as a calibrated safety forecast
12
The delivered run is internally coherent: the conditional analytical model predicts 84,724 episodes; simulation produced 84,296 (within 0.5%).
What the results support
• Sensitivity analysis of layer rates and dwell times
• Comparing coverage strategies
• Identifying which conditions drive exposure
• Testing episode definitions and overlap handling
Critical interpretation caveat
The analytical report’s 1.639% “unknown-time union” is element-only. It is not directly comparable with the simulated 2.741% union once pattern and hash combinations are enabled.
Bottom line: the run quantifies exposure to the model’s definition of unknownness—not empirical AV danger or failure probability.
Sources: analytical_model.py; analytical_model.md; results/summary.md