## Slide 1
SCENARIO COVERAGE · SIMULATION STUDY · AUGUST 2026
Does the Occurrence of Unknown Scenarios
Follow a Poisson Distribution?
A layered-scenario simulator for autonomous-vehicle validation — project purpose, simulator design, and results
Samer Jameel · Xinhai Zhang
Scenario Coverage work stream
STREET
street_009
TEMPORAL
temporal_030
EGO MAN.
ego_011
RU MAN.
ru_010
ENVIRONMENT
environment_004
TRIGGERING
trigger_014
one simulated scenario state — the active rare set {ego_011, ru_010, trigger_014} matches a selected C3 rule and opens an unknown-scenario episode

## Slide 2
OVERVIEW
What this presentation covers
2
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
01
Purpose & motivation
Why the Poisson assumption matters for AV validation mileage and acceptance criteria — and why it can only be tested in simulation.
02
The simulator
A six-layer scenario world: generated elements, three rarity classes, exact probability masses, per-element Gamma durations.
03
How a run works
The event loop, the exact C3–C6 rare-combination mechanism, and a worked example of an episode's life cycle.
04
Results & discussion
The 20,000-hour reference run, Poisson diagnostics, the verification battery, sensitivity studies — and what it all means.

## Slide 3
PURPOSE
Verify the Poisson assumption behind the AV safety case
3
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Plus AI assumes that manifestations of functional insufficiencies (FIs) follow a Poisson distribution.
That single assumption underpins two safety-case calculations:
Validation mileage — how many miles are enough to demonstrate the residual FI rate is acceptably low.
Decomposition of acceptance criteria — splitting a vehicle-level target across scenario classes and subsystems.
Goal of this work
Verify the validity of this assumption — does the occurrence of unknown scenarios really follow a Poisson distribution?
Source: problem definition, “Poisson Assumption Verification” (Jameel & Zhang).
The test at the heart of it
Count unknown-scenario occurrences k in fixed mileage windows, then compare Var(k) with Mean(k).
Var(k) ≫ Mean(k)
Overdispersion — risky: bursts of failures; needs more validation miles
Var(k) ≈ Mean(k)
Poisson-consistent — the assumption and the mileage math hold
Var(k) ≪ Mean(k)
Underdispersion — too conservative: mileage targets overshoot

## Slide 4
PURPOSE
Testing it needs far more miles than any fleet can drive
4
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
FIs are triggered by scenarios. Autonomous driving is a chain of scenarios; an FI manifests when the vehicle meets a scenario it cannot handle — so scenario occurrence is what must be modeled.
Unknown scenarios are rare. In the simulated world: one episode every ≈2,000 miles. Real-world rates are far lower still.
Dispersion needs replication. Estimating Mean(k) and Var(k) takes hundreds of independent mileage windows — tens of millions of miles. “Can only be done in simulation.”
Poisson has a testable signature. If counts are Poisson, the miles between successive occurrences are exponential and windows are independent — both directly checkable on simulator output.
Miles between FIs — exponential if Poisson
0
0.5
1
1.5
2
2.5
3
3.5
✕
✕
✕
✕
✕
✕
✕
driven mileage (million miles)
✕ = unknown-scenario occurrence — gaps should be memoryless (exponential)
20,000 h
simulated per run — in 11.7 s of wall-clock time
1M miles
of driving history per run at 50 mph average
→ the simulator turns a fleet-scale question into minutes of compute

## Slide 5
BACKGROUND
A driving scene = six layers, one active element each
5
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
street
road geometry / section type
12 elements
temporal_modifications
work zones, temporary traffic management
45 elements
ego_maneuver
ego vehicle maneuver classes
20 elements
ru_maneuver
surrounding road-user maneuvers
22 elements
environmental_conditions
weather, visibility, light
22 elements
triggering_conditions
unexpected AV triggering conditions
83 elements
Layer structure follows the PEGASUS-style layered scenario model used in TRATON. The scene at any instant is the cross product of the six active elements; driving is a chain of such scenes.
Where can an unknown scenario come from?
Unknown element in a known layer
a phenomenon the taxonomy has no entry for
Unknown layer
a whole dimension missing from the model
Unknown combination of known elements
each element is known — their joint occurrence was never anticipated
MODELED IN V6
The simulator focuses on the third cause: it plants specific rare-element combinations as the “unknowns” and measures how often the driving process stumbles into them.

## Slide 6
THE SIMULATOR
An event-driven, fully reproducible six-layer world
6
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
config.yaml
class percentages, duration profiles, rule counts, 7 independent seeds
→
Build the world
generate elements & rarities per layer; exact class masses; one Gamma law per element; select 100 C3–C6 rules
→
Event loop
jump from layer expiry to layer expiry; resample expired layers; advance time & miles
→
Episodes
open when the active rare set exactly matches a selected rule; close when the match breaks
→
Outputs
episodes.csv, windows.csv, summary.md, stats.json, diagnostic plots
6
independent layers, each holding one active element
204
generated elements (this build): 145 common · 40 rare · 19 unknown
100
planted rare-combination rules: C3 40 · C4 30 · C5 20 · C6 10
7
seed streams — same config ⇒ bit-identical run (checkpoint-safe)
39
automated tests pass; config validation rejects invalid setups
Semi-Markov world: layers evolve independently; “unknown” rarity-class elements exist but never open episodes by themselves in v6 — only exact rare combinations do.

## Slide 7
THE SIMULATOR
Building the world: controlled rarity in every layer
7
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
layer
count range
built
common / rare / unknown
baseline mean
street
12
12
9 / 2 / 1
300 s
temporal_modifications
40–45
45
32 / 9 / 4
600 s
ego_maneuver
20–24
20
14 / 4 / 2
30 s
ru_maneuver
20–24
22
16 / 4 / 2
45 s
environmental_conditions
22
22
16 / 4 / 2
1,800 s
triggering_conditions
80–90
83
58 / 17 / 8
120 s
Element counts are drawn per layer from the configured range (seeded); IDs are stable: street_000, ego_003, trigger_042 …
Class counts use the largest-remainder method on the configured 70 / 20 / 10 split — integer counts, always ≥ 1 per class.
Across all six layers
145
common elements
71.1% of 204 — target 70%
40
rare elements
19.6% of 204 — target 20%
19
unknown elements
9.3% of 204 — target 10%
Note — unknown-class elements occur in ~10% of selections, but in v6 they never open episodes themselves; they only disqualify a rare-combination match while active.

## Slide 8
THE SIMULATOR
Who comes next: exact class masses, varied within class
8
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Permanent transition vector per layer. When a sojourn expires, the next element is drawn from the layer's fixed probability vector — independent of all other layers (self-transitions allowed).
Class masses are pinned exactly. selection_class_percentages fixes common / rare / unknown total probability at 70% / 20% / 10% — by construction, not on average.
Variation inside a class. One Dirichlet(c·p) draw (c = 20,000) makes elements unequal; each class is then rescaled back to its exact mass — jitter changes only the within-class split.
Initial state uses the same exact class totals; every random source has its own seed stream.
Worked example — triggering_conditions
rare class mass (configured)
20.000%
rare elements in this layer
17
equal-split baseline per element
≈ 1.18%
after seeded Dirichlet jitter
≈ 1.05 – 1.31% each
class total after rescaling
exactly 20.000%
Verified in the run: every layer's realized transition mass is 10.0000% unknown / 20.0000% rare / 70.0000% common; empirical unknown selection share 10.02% vs 10% design target.

## Slide 9
THE SIMULATOR
How long an element persists: one Gamma law per element
9
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
μᵢ = μ_layer × m_rarity × (1 + spread · uᵢ)
σᵢ = CV_rarity · μᵢ Gamma: shape = μᵢ²/σᵢ², scale = σᵢ²/μᵢ
uᵢ ∈ [−1, 1]: stable position of element i inside its class band · clamp ≥ 1 s
class
mean multiplier
CV
spread
common
1.50 ×
0.45
±10%
rare
0.75 ×
0.60
±10%
unknown
0.25 ×
0.80
±10%
Bands never overlap within a layer: every common mean > every rare mean > every unknown mean — unknown states are brief by design.
Gamma shape κ = 1/CV² ≈ 1.6–4.9, so sojourns are more regular than exponential.
Simulator output — duration_distributions/triggering_conditions.png. Layer baseline 120 s → representative means: common 179.7 s, rare 90.0 s, unknown 29.6 s.

## Slide 10
HOW A RUN WORKS
The event loop: jump from expiry to expiry, never tick seconds
10
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
1
Find the next event
dt = min over layers of remaining sojourn time (clipped at the 20,000 h horizon)
2
Advance the world
t += dt; miles += 50 mph × dt / 3600 — mileage is derived, time is the clock
3
Resample expired layers
draw the next element from the layer's vector; draw its own Gamma duration
4
Evaluate the rules
compare the new active rare set against the 100 planted combinations; open / continue / close an episode
4,079,575 events cover 20,000 h (one event per ≈18 simulated seconds) — 11.7 s wall-clock.
six independent sojourn clocks
street
temporal
ego man.
ru man.
environment
triggering
one event: a layer expires → only that layer resamples; the other five clocks keep running
common
rare
unknown

## Slide 11
HOW A RUN WORKS
Unknown scenarios = exact combinations of known rare elements
11
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
100 rules planted at build time — C3: 40, C4: 30, C5: 20, C6: 10 — sampled uniformly without replacement (ordinal unranking; no Cartesian blow-up).
Every rule spans distinct layers with one rare element per layer, and always includes a rare triggering condition.
Rule mass = product of its members' probabilities. C3 masses ≈ 0.001–0.006%; C5/C6 masses ≈ 10⁻⁸ — planted but effectively never met.
A self-transition that leaves the rare set unchanged continues the open episode — it does not close or re-open it.
Why “exact” matching?
A rule matches only when the complete active rare set equals it. A C3 inside a richer rare state does not fire — no double counting, and every episode is attributable to exactly one rule.
Does the current state match a rule?
Active rare set = the rule's set, exactly
every rule element active; no extra rare element anywhere
No unknown-class element active
an unknown element in any layer disqualifies the match
All remaining layers are common
follows from the two conditions above
Match → open (or continue) an episode
stays open while the match persists — self-transitions do not close it; closes on the first breaking change

## Slide 12
HOW A RUN WORKS
Worked example: the life of episode #1 (real run data)
12
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Rule C3: ego_maneuver = ego_011 & ru_maneuver = ru_010 & triggering_conditions = trigger_014 · mass 0.0031% · 27 episodes in this run · common-layer chips illustrative
MILE 2,269.8 — EPISODE OPENS
STREET
common
TEMPORAL
common
EGO MAN.
ego_011
RU MAN.
ru_010
ENVIRONMENT
common
TRIGGERING
trigger_014
trigger_014 is drawn at a triggering-layer expiry → active rare set now equals the rule exactly → unknown-scenario episode opens.
WHILE THE MATCH PERSISTS
STREET
common′
TEMPORAL
common
EGO MAN.
ego_011
RU MAN.
ru_010
ENVIRONMENT
common
TRIGGERING
trigger_014
Common layers may transition to other common elements; the rare set is unchanged → the same episode continues (no re-count).
23.9 s / 0.33 mi LATER — EPISODE CLOSES
STREET
common
TEMPORAL
common
EGO MAN.
ego_011
RU MAN.
ru_010
ENVIRONMENT
common
TRIGGERING
trigger_083
trigger_014 expires and a common trigger replaces it → rare set no longer equals the rule → episode closes; start, end, duration written to episodes.csv.
No match if: an extra rare element is active (rare set ≠ rule) · any unknown-class element is active · only a subset of the rule is present

## Slide 13
HOW A RUN WORKS
Count episodes, not encounters — the change that made counts testable
13
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Before (v1): per-tuple encounters
Every new element tuple seen during one unknown period was counted as a fresh “encounter”.
Fast layers churn while a slow unknown persists → bursts of counts from a single real condition.
Windows shared bursts → heavily clustered counts, nothing like Poisson.
Since v2 (kept in v6): episodes
One episode = one maximal continuous period during which the unknown condition persists.
Opens are rare, short, well-separated events — the natural analogue of “one FI manifestation.”
In v6: the period during which the active rare set stays equal to one rule.
D ≈ 12
encounter counts — strongly clustered (early runs)
→
D ≈ 1
episode starts — near-Poisson dispersion
D = Var / Mean of counts per 10,000-mile window

## Slide 14
THE SIMULATOR
The simulator does exactly what the configuration says
14
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Seven independent seed streams (element counts, rarity placement, Dirichlet, durations, initial state, transition sampling, rule selection) — the same config always reproduces the identical run.
Checkpoint / resume is bit-identical to an uninterrupted run — long horizons can be chunked safely.
39 automated tests pass, covering validation, exact-set matching, triggering-condition inclusion, unknown disqualification, exact time stop, and resume.
Realized behavior matches configured targets: class masses exact by construction; empirical unknown selection 10.02% vs 10%; per-layer realized mean sojourns within ≈4% of configured (e.g. street 381 s cfg → 366 s emp).
Simulator output — configured vs realized vs empirical class shares, per layer (plots/class_mass_verification.png)

## Slide 15
THEORY
Why Poisson is the expected answer — conditional on a built world
15
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
1 · ONE LAYER
Thinned renewal → exponential
Each transition opens an episode with small probability p; the wait between opens is a geometric sum of Gamma sojourns. Rényi (1956): as p → 0 the normalized gaps converge to Exp(1) — the opens form a Poisson process of rate p/μ.
2 · SIX LAYERS
Superposition stays Poisson
Layers are independent by construction. Grigelionis: the union of independent near-Poisson streams converges to a Poisson process with the summed rate Λ = Σ (mₖ − sₖ)/μₖ. Disjoint windows become independent.
3 · FINITE P
The correction is invisible
For a thinned renewal stream, dispersion → 1 − p(1 − 1/κ). At p ≈ 0.004 and Gamma κ ∈ [1.8, 4]: a 0.18–0.30% deviation — an order of magnitude below the sampling noise of any realistic window count.
Two boundaries of the claim. (1) It is conditional on one built world — across construction seeds, counts are mixed Poisson and genuinely overdispersed. (2) The proof thins transitions i.i.d.; v6's exact-combination matching depends on the joint cross-layer state — the results section measures what that does.
Full derivation: poisson_proof.md (renewal theory + Chen–Stein bound for the 1-dependent indicators).

## Slide 16
RESULTS
The v6 reference run: 20,000 hours, one million miles
16
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
495
unknown episodes in 1M miles — one every ≈2,020 mi (≈40 h)
0.0144%
of driving time inside an unknown scenario (10,362 s total)
20.9 s
mean episode duration · median 16.4 s · p90 42.6 s (≈0.29 mi)
C3: 481
episodes from C3 rules · C4: 14 · C5/C6: 0 (too rare to observe)
Simulator output — cumulative episodes: steady, linear accumulation with no drift.
48 of the 100 planted rules fired at least once; the top rule produced 38 episodes (it contains slow street-layer elements).
All 495 episodes are rare-combination episodes — the only unknown mechanism in v6; none were truncated at the horizon.
Rates are properties of the configured world (design defaults, not field calibration). The object under test is the distributional shape of the counts, not the absolute rate.

## Slide 17
RESULTS
Window counts: the shape fits Poisson, the variance runs high
17
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Simulator output — episode starts per 10,000-mile window across the run (99 complete windows).
mean 4.93 · var 6.68
counts per 10,000-mile window
D = 1.355
dispersion index — ≈35% above the Poisson value of 1 (two-sided p ≈ 0.02: borderline)
GOF p = 0.82
χ² goodness of fit vs Poisson(4.93): the marginal shape is fully compatible
A single run gives only 99 windows — under Poisson the dispersion estimate itself has sd ≈ 0.14, so 1.355 is a signal worth explaining, not yet a verdict.

## Slide 18
RESULTS
Inter-arrival gaps expose fine-scale clustering
18
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Simulator output — survival curve and Q–Q of the 495 inter-arrival times vs the fitted exponential.
The mechanism. Slow layers hold rare elements in place for minutes (street ≈ 6 min, temporal ≈ 12 min, environment ≈ 37 min mean sojourns). A fast layer briefly breaks the match, then re-completes it — one persistent real-world condition is logged as several episodes in quick succession.
KS p < 0.001
exponential fit rejected (KS = 0.112, n = 495); CV² of gaps = 1.20
37 gaps < 1 mile
vs ≈0.3 expected under exponential — a large excess of near-immediate re-arrivals
46 of 73
gaps under 100 mi are the same rule re-opening moments after it closed
Gap analysis computed from the run's episodes.csv.

## Slide 19
RESULTS
Count distinct manifestations — and Poisson is restored
19
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Treat re-opens of the same rule within 10 miles as one manifestation — the episode-level analogue of “the same FI condition, briefly interrupted.” This merges 45 of 495 starts (9%).
RAW EPISODE STARTS (495)
D = 1.355
dispersion, p ≈ 0.02
KS p < 0.001
exponential rejected
→
MERGED MANIFESTATIONS (450)
D = 1.084
dispersion, p = 0.53
KS p = 0.84
exponential fits
Reading: the entire measured deviation is re-opening bookkeeping, not genuine clustering of distinct unknown conditions. At the level that matters for the safety case — distinct manifestations — the v6 run is statistically indistinguishable from a Poisson process (dispersion p = 0.53, exponential-gap p = 0.84). The result is robust to the merge window: 10–100 mi all give the same answer.
Recomputed from episodes.csv / windows.csv of the v6 reference run (same tests as poisson_tests.py).

## Slide 20
RESULTS
The formal verification battery: all tests pass
20
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
poisson_tests.py ran the decisive experiments on the element-route configuration (the mechanism the proof covers, ≈20× higher episode rate — much more statistical power):
A · Replication PASS
300 independent runs × 3,000 mi over the same built world (only run-time seeds vary): mean 58.6, dispersion 1.078 (p = 0.34); χ² GOF vs Poisson: p = 0.14.
B · Windows PASS
200 disjoint 10,000-mi windows of a 2M-mile run: dispersion 0.956 (p = 0.68) — no over- or under-dispersion.
C · Gaps PASS
39,227 inter-arrival distances vs exponential: KS = 0.0055, p = 0.18 — memoryless gaps ⇔ Poisson process.
poisson_proof.png — replication counts vs Poisson PMF · window counts vs Poisson PMF · Q–Q of gaps vs exponential

## Slide 21
RESULTS
21 parameter studies: what actually moves the episode rate
21
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Study output — one-factor sensitivity: effect range ÷ seed-only standard deviation (SNR).
Scale: 21 component studies · 1,160 simulations · ≥10 levels per numeric control · 3 replicates per level.
Dominant drivers of the unknown-episode rate: element class percentages (SNR 123), selection class percentages (46), combination counts (19), rarity duration multipliers (9).
Null checks behave: average speed and mileage-window size have exactly zero effect — they only relabel the same time axis, as designed.
Seed noise is large: seed-only sd of the rate is ≈28% of its mean — single-run rates carry real construction uncertainty (→ discussion).
Caveat: screening ranges are deliberately wide; the ranking describes tested ranges, not unit-free importance.

## Slide 22
DISCUSSION
So — is the Poisson assumption safe?
22
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6
Supported
Conditional on a fixed world model, unknown-scenario manifestations are Poisson: proven in the rare-event limit, confirmed by the full test battery, and — after merging same-rule re-opens — by the v6 run itself (D = 1.08, KS p = 0.84). Miles between manifestations are exponential, exactly as the validation-mileage math assumes.
One nuance
Raw v6 episode counts are ≈35% overdispersed (D = 1.355). Cause identified: the same rule re-opens within persistent slow-layer states. Definitional fix: count manifestations (debounced episodes), or carry the measured dispersion factor into the mileage budget as a safety margin.
Real caution
Across differently-built worlds the counts are mixed Poisson — overdispersed by construction (seed-only rate sd ≈ 28%). A validation-mileage figure derived from one Poisson rate understates uncertainty about the world itself. Budget for model uncertainty, not just within-model noise.
Practical recommendation: base validation mileage on manifestation-level counts; where conditions are heterogeneous or the model uncertain, inflate targets by the measured dispersion index.

## Slide 23
CONCLUSIONS
Poisson holds where it is needed — and the exceptions are now understood
A verified instrument
A reproducible six-layer scenario simulator: exact class masses, per-element Gamma durations, planted C3–C6 unknowns, 1M-mile histories in seconds, 39 tests.
The assumption verified
Within a fixed world, unknown-scenario manifestations are Poisson — proven in the rare-event limit, confirmed by replication, window, and gap tests.
The deviation explained
Raw v6 overdispersion (D = 1.35) traces entirely to same-rule re-opens inside persistent slow-layer states; merged manifestations restore D = 1.08.
The boundary that matters
Across model builds, counts are mixed Poisson — validation mileage and acceptance-criteria decompositions should budget for world-model uncertainty.
Future work: calibrate layer catalogs and durations to field data · interaction studies beyond one-factor screening · conditional transition mode · multi-seed dispersion confidence intervals
Artifacts: simulator.py · config.yaml · episodes.csv / windows.csv / stats.json · poisson_proof.md · 21 studies under studies/
23
Unknown-Scenario Poisson Verification · Layered Scenario Simulator v6